## Slide 1: SCIENTIFIC TOOLS

## Slide 2: Microscopes
Light Microscope – (optical microscope) – Uses light to produce an enlarged view of a specimen.
Magnification – Magnifying Power – How large an image looks under the microscope.
  Specimens are magnified by the objective lens and/or the occular (eyepiece)
RESOLUTION – the sharpness of an image. Resolution is increased on high power.
  An image is “resolved” by using the fine adjustment (focus) knob.

## Slide 3: TYPES OF MICROSCOPES
Simple Microscope – magnifying glass
Compound Microscope – Uses two lenses: objective and ocular.
Stereomicroscope – a.k.a. Dissecting Microscope
  Used to view specimens too big for a compound light microscope

## Slide 4: COMPOUND MICRSCOPE - OPTICAL SYSTEM
Objectives – usually 2-3 for low power, medium power and high power.
    High power has a magnification of 40X (X means “times”)
    Medium power magnification is 10X
    Low power magnification is 4X
Ocular is the part that you look through.
  Magnification is 10X
To calculate TOTAL magnification, multiply the ocular (10X) by the objective magnification.
  Example: TOTAL magnification on high power would be 10 X 40 = 400 X

## Slide 5: COMPOUND MICROSCOPE - MECHANICAL SYSTEM
Structural parts of the microscope.
Base – microscope stand.
Stage – platform where the slide is placed.
Stage clips – two metal clips that hold the slide in place.
Body tube – contains the lenses.
Eyepiece – at the top of the body tube.
Nosepiece – At the bottom of the body tube and holds the objectives.
  By turning the nosepiece, the objectives are moved.

## Slide 6: COMPOUND MICROSCOPE - MECHANICAL SYSTEM (cont’d)
Focusing – Two adjustment knobs are used to focus the microscope.
Coarse focus – Large knob and is used to initially bring the specimen into clear view.
IT IS USED ON LOW POWER ONLY. – WHY???
THE STAGE MOVES WITH THE COARSE FOCUS AND ON HIGH POWER IT COULD BREAK THE SLIDE AND DAMAGE THE OBJECTIVE
Fine focus – small knob and is used for “fine tuning” (resolution) the specimen. This is used at the high and low powers.
WHEN USING THE HIGH POWER OBJECTIVE, ONLY USE THE FINE FOCUS.

## Slide 7: COMPOUND MICROSCOPE - MECHANICAL SYSTEM (cont’d)
Illuminator – The light source located on the base of the microscope.
Diaphragm – mounted just below the stage and is used to regulate the amount of light on the specimen.

## Slide 8: STEREOMICROSCOPE –DISSECTING MICROSCOPE
Contains two eyepieces and provides a more 3-dimensional image of the specimen.
It is used for dissecting small organisms or small parts of organisms.
Used in ecological studies.

## Slide 9: STEREOMICROSCOPE

## Slide 10: LIGHT MICROSCOPE
Coarse focus
Fine focus
Arm
Stage clip
Base
Occular or eyepiece
Body tube
Revolving nosepiece
Objective
Objective
Stage
Diaphragm
Light source (illuminator)
1
2
3
4
5
6
7
8
9
10
11
12
13